## Slide 1: ZAS Academy
Python Curriculum for IOT & AI

## Slide 2: Day1 - Agenda
Day 1
Introduction to Raspberry PI
Raspberry PI OS Installation
Connect to Raspberry PI

## Slide 3: Day1 – Computer Architecture

## Slide 4: Day1 – Computer Architecture

## Slide 5: Day1 – Operating System

## Slide 6: Day1 – Preparing PI for Action
Step-1: Format the SD Card
Step-2: Burn the OS Image on to the SD Card
Step-3: Create an empty file called “ssh”
Step-4: Insert the SD Card into PI and Bootup
Step-5: Connect to Raspberry PI (via Terminal/Putty)
Step-6: Update/Upgrade OS
Step-7: Change Raspi-Configuration: enable VNC, Resolution and Restart
Step-8: Enable WIFI, Configure Screen Resolution
Step-9: Connect to PI using VNC Viewer
Step-10: Update/Install Software on Raspberry PI

## Slide 7: Day1 – Download Software
SD Card Formatter
Etcher
Raspbian OS Image
FileZilla FTP Client (if you don’t have)
VNC Viewer

## Slide 8: Day1 – Required Hardware
SD Card (16/32 GB at least)
SD Card Reader
Raspberry PI 3 – B/B+ or PI4

## Slide 9: Day1 – Download Software – SD Card Formatter
https://www.sdcard.org/downloads/index.html

## Slide 10: Day1 – Download Etcher
https://www.balena.io/etcher/

## Slide 11: Day1 – Download Software – VNC Client
https://www.realvnc.com/en/connect/download/viewer/raspberrypi/

## Slide 12: Day1 – Download Software – Raspberry PI Image - Raspbian
https://www.raspberrypi.org/downloads/raspberry-pi-os/
https://www.youtube.com/watch?v=toWBmUsWD6M

## Slide 13: Day1 – Step-1: Format SD Card
Insert SD Card into your laptop
Launch SD Card Formatter app
Select quick format
And click on format

## Slide 14: Day1 – Step-2: Copy Raspberry PI Image to SD Card Using Etcher
Launch Balena Etcher App
Select Image
Select SD Card
Click on Flash

## Slide 15: Day1 – Step-2: Copy Raspberry PI Image to SD Card Using Etcher
Launch Balena Etcher App
Select Image
Select SD Card
Click on Flash

## Slide 16: Day1 – Step-2: Copy Raspberry PI Image to SD Card Using Etcher
Launch Balena Etcher App
Select Image
Select SD Card
Click on Flash

## Slide 17: Day1 – Step-3 Create Empty File called: ssh
With SD card still plugged into laptop
Create an empty file called “ssh” and save it on to SD card drive. You can use any of your favourite text editor like – textmate/notepad/text editor etc.
Note: This is required so the SSH server can start automatically when we power on PI

## Slide 18: Day1 – Step-3 Create Empty File called: ssh

## Slide 19: Day1 – Step-4: Power on PI
Insert SD Card inserted into PI
Connect PI to your Wi-Fi router using the RJ45 Network Cable
Power on PI using USB-C cable

## Slide 20: Day1 – Step 5: Options to Connect to Raspberry PI
Option A->VNC Viewer Client
Option B -> SSH Client
(Putty on Windows or
Terminal on Mac)
To Connect to PI , We need one of them
SSH Server Running
VNC Server Running
But By Default –
SSH Server is not running and disabled (therefore, we need to create an file called “ssh” in the Pi Image SD Card so server starts up automatically).
VNC Server is not installed
1
2
3
4
5

## Slide 21: Day1 – Step:4 Power ON Raspberry PI
Power on Raspberry PI
Insert the SD Card Prepared Earlier into the Raspberry PI
Connect the Network Cable (RJ45) from router to raspberry pi network port
Power on the Raspberry PI

## Slide 22: Day2 – Step-5: Finding IP Address of Raspberry PI – 2 Options
Find IP Address of Using IP Scanner
MAC: https://angryip.org/
Windows: https://www.advanced-ip-scanner.com/
Find IP Address of Raspberry PI (via Router)
1. Connect to your router: the connection string might look something like the below:
192.168.0.1

## Slide 23: Day2 – Step-5: Connect to Raspberry PI Using Terminal or Putty
ping raspberrypi.local
ssh <ip address>
Raspberry PI Username and Password are below
User Name: pi
Password: raspberry

## Slide 24: Day2 – Step-5: Connect to Raspberry PI Using Terminal or Putty
ping raspberrypi.local
MAC Computer
  Open the terminal window and run the following command
  ssh pi@<ip address>
Windows PC
  Launch Putty (see the screen print below)
  Raspberry PI Username and Password are below
    User Name: pi
    Password: raspberry
Windows PC

## Slide 25: Day2 –Step-6: VNC Server Installation on PI
Run the following commands
sudo apt-get update
sudo apt-get upgrade
  This command will ask you Y/n question  please type Y
This takes some time (5-10 mins)

## Slide 26: Day2 –Step-6: VNC Server Installation on PI
Run the following commands
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install tightvncserver
Start the vnc server by running the following command
vncserver :1
It will prompt for password set it as: raspberry
For view only password type – n
NOT REQUIRED for PI-4

## Slide 27: Day2 – Step-6: Configure VNC Server To Start Automatically
1. Using Terminal/Putty login to Raspberry PI device
2. Edit the following file
sudo vi /etc/rc.local
In the file add the following line just before
the last line (screen print below)
sudo – pi –c '/usr/bin/vncserver :1’
3. Save the file
4. Reboot the device by running the following
command
sudo reboot
https://www.youtube.com/watch?v=JYKZjUgtOYw
NOT REQUIRED for PI-4

## Slide 28: Day2 – Step-7: Enable VNC Server Connections
Run the following commands
sudo raspi-config
https://www.youtube.com/watch?v=JYKZjUgtOYw
1
2
3
4

## Slide 29: Day2 – Step-7: Change Screen Resolution
1
2
3
4

## Slide 30: Day2 – Step-8: Wired Connection to PI using VNC Client - Enable WiFi
Launch VNC Client
1
2
3
4

## Slide 31: Day2 – Step-8: Wired Connection to PI using VNC Client - Enable WiFi
Launch VNC Client
4
5

## Slide 32: Day2 – Step-9: Enable WiFi
Click on the WiFi Icon
Connect to your WiFi Network (it may prompt for wifi password)

## Slide 33: Day2 – Step-9: Enable WiFi

## Slide 34: Day2 – Step-9: Enable WiFi
1
2
3
4

## Slide 35: Day2 – Step-10: Power ON Raspberry PI and Wireless Connection using VNC
Disconnect the PI from the Router (unplug the RJ45 cable)
Power on the PI
Wait for couple of minutes
Launch the VNC Viewer
Create a new connection and connect
Raspberry PI Username and Password are below
  User Name: pi
  Password: raspberry

## Slide 36: Day2 – Step-10: Download Software – VNC Client
Extra slides (this is already repeated in prev slides

## Slide 37: Day1 – Step-10: Connect to Raspberry PI Using VNC Client
Extra slides (this is already repeated in prev slides

## Slide 38: Day1 – Step-10: Connect to Raspberry PI Using VNC Client
Extra slides (this is already repeated in prev slides

## Slide 39: Day1 – Step-11: Software Installation on PI
Python3 should have been already installed on Raspberry PI. Please check by running the following command. If not installed follow the instructions at the link - http://www.knight-of-pi.org/installing-python3-6-on-a-raspberry-pi/
python3 --version

## Slide 40: Day2 – Some useful unix commands (MAC Computers)
https://www.dnsstuff.com/scan-network-for-device-ip-address
ipconfig
ifconfig
arp -a
To delete the finger print of SSH connection
ssh-keygen -R "hostname or ip-address"

## Slide 41: Day2 – Some useful unix commands (how to remove ssh fingerprint)
ssh-keygen -R "hostname or ip-address"
1
2
3
4
ssh pi@hostname/ipaddress
Connection failed
5

## Slide 42: Day1 – Step-9: Install Python Libraries for DHT11 Sensor on PI
Connect to PI
Run the following commands to install Python Libraries for DHT11 Sensor.
Reference Link: https://github.com/adafruit/Adafruit_Python_DHT
sudo pip3 install Adafruit_DHT

## Slide 43: Day1 – DHT11 - Wiring
https://www.raspberrypi-spy.co.uk/2017/09/dht11-temperature-and-humidity-sensor-raspberry-pi/
You Can Use PIN2 which is 5V (as shown in the PIN Diagram)
Please pay attention to PIN Numbers and the corresponding GPIO xx numbers

## Slide 44: Day1 – Run DHT11 Python Script To See the Values from Sensor
Create a folder called AWS_IOT on PI
  mkdir AWS_IOT
Change into the directory AWS_IOT folder
  cd AWS_IOT
Copy the TemptDHT11.py script to AWS_IOT folder (you may use FileZilla FTP Client to connect to PI and Transfer the files). Screen print of FileZilla is shown on the next slide
  python3 TempDHT11.py

## Slide 45: Day1 – Download Software – FTP Client
See the Section FTP Client Installation & Configuration
To Connect to Raspberry PI Board (this step required later)
IP Address of Raspberry PI: 192.168.?.?
User: pi
Password: raspberry
Port: 22

## Slide 46
https://filezilla-project.org/download.php?platform=osx
FTP Client Installation

## Slide 47
Logistics
Lecture | Date | Day | Time | Comments
1 | 15-Aug-2010 | SAT | 09:00AM | 
2 | 22-AUG-2020 | SAT | 09:00AM | 
3 | 29-AUG-2020 | SAT | 09:00AM | 
4 | 05-Sep-2020 | SAT | 09:00AM | 
5 | 12-Sep-2020 | SAT | 09:00AM | 
 | 19-Sep-2020 | SAT | 09:00AM | Midterm Exams
6 | 26-Sep-2020 | SAT | 09:00AM | 
7 | 03-OCT-2020 | SAT | 09:00AM | 
8 | 10-OCT-2020 | SAT | 09:00AM | 
9 | 17-OCT-2020 | SAT | 09:00AM | 
 | 24-OCT-2020 | SAT | 09:00AM | Dasara Break
 | 31-OCT-2020 | SAT | 09:00AM | Dasara Break
10 | 07-NOV-2020 | SAT | 09:00AM | 
 | 14-NOV-2020 | SAT | 09:00AM | Diwali Break
11 | 21-NOV-2020 | SAT | 09:00AM | 
12 | 28-NOV-2020 | SAT | 09:00AM |